## Slide 1
Delft University of Technology
Challenge the future
1
Deployability of Content-Centric Networking
Group 3 :
Mani Prashanth Varma Manthena (4243846)
Michal Golinski (4253590)
Dr. ir. Fernando Kuipers
Niels van Adrichem
(Network Architectures and Services Group)

## Slide 2: Introduction
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
TCP/IP (host based communication model) vs. CCN (content-centric networking)
Problem description :
Deployability considerations of CCN like content to cache, cache size, caching under changing link conditions, etc.
To compare CCN performance with present TCP/IP architecture under various simulated real world scenarios.

## Slide 3: Outline
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Related work
The Project CCNx
Measurement scenario
Measurement results
Conclusion and future work

## Slide 4: Related work
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Cache size implementation and memory management of CCN based on various aspects like memory blocks price, efficiency of memory storage and buffering, amount of traffic in the network, etc.
Performance comparison of CCN with TCP/IP e.g. data transfer efficiency comparison of CCN, HTTP and HTTPS – Van Jacobson (2009).
Performance comparison of CCN with TCP/IP for various real time services and applications like live streaming, audio and video distribution, etc.

## Slide 5: The Project CCNx
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Introduction
Comparison of IP and CCN protocol stack
CCN packet types – interest and data
CCN content naming – hierarchical structure
figure: Van Jacobson (2009)

## Slide 6
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
CCN forwarding engine model
Project CCNx allows users to change several CCN protocol parameters like cache size, MTU size, etc. in the protocol open source configure file.
figure: Van Jacobson (2009)

## Slide 7: Measurement scenario
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Measurement setup – A
Measurement setup - B

## Slide 8
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Measurement setup – C
Measurement setup - D

## Slide 9
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Problems encountered – delay measurements, hardware configuration, MTU not responding
Expected results
Larger cache sizes would decrease overall delay, jitter, etc. in measurement setups C and D.
CCN would out perform HTTP in measurement setups C and D and would approximately match the performance of HTTP in other setups and scenarios.
MTU size could fix the problem of decrease of bandwidth.
CCN could handle packet losses like TCP/IP.

## Slide 10: Measurement results
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Influence of cache size on delay
Mean packet delays
Chart: Mean packet delays
| 10 | 5000 | 10000 | 20000 | 50000
No delay | 7.5034 | 8.1431 | 10.5055 | 9.0552 | 8.7384
No delay - second download | 8.3365 | 8.4745 | 8.5059 | 3.3678 | 3.0825
Delay 100ms | 115.2203 | 115.091 | 119.1114 | 116.2191 | 122.3458
Delay 100ms - second download | 115.6797 | 114.7016 | 117.0853 | 4.1672 | 7.4806
Delay 200ms | 221.234 | 222.1111 | 222.4028 | 220.7966 | 221.2485
Delay 200ms - second download | 221.0444 | 221.1717 | 222.9332 | 2.9693 | 3.2957

## Slide 11: Standard deviation of packet delays (jitter)
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Chart: Standard deviation of packet delays
| 10 | 5000 | 10000 | 20000 | 50000
No delay | 2.8979 | 3.3051 | 7.2335 | 4.8591 | 5.3519
No delay - second download | 3.7317 | 3.7994 | 3.4183 | 2.2745 | 1.6971
Delay 100ms | 5.3796 | 6.3021 | 10.0867 | 14.8028 | 38.7022
Delay 100ms - second download | 7.7977 | 6.5075 | 7.5094 | 14.7781 | 11.8119
Delay 200ms | 9.291 | 10.8557 | 8.7278 | 7.4591 | 8.5143
Delay 200ms - second download | 9.3426 | 8.8456 | 9.9656 | 1.3962 | 2.1504

## Slide 12
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Influence of delay on a bandwidth
Bandwidth of file download (logarithmic scale)
Chart: Bandwidth of file download
| 0 ms | 100 ms | 200 ms
HTTP | 4.84 | 2.48 | 1.85
CCN, cache size 10, first download | 0.20795 | 0.095227 | 0.061186
CCN, cache size 10, second download | 0.18375 | 0.08143 | 0.062349
CCN, cache size 10000, first download | 0.17057 | 0.091139 | 0.051152
CCN, cache size 10000, second download | 0.15053 | 0.095474 | 0.060588
CCN, cache size 20000, first download | 0.1533 | 0.10085 | 0.061654
CCN, cache size 20000, second download | 0.15935 | 0.15923 | 0.19084

## Slide 13
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Relative bandwidth loss
Chart: Relative bandwidth loss
| 0 ms | 100 ms | 200 ms
HTTP | 1 | 1.9516 | 2.6162
CCN, cache size 10, first download | 1 | 2.1837 | 3.3986
CCN, cache size 5000, first download | 1.1991 | 2.3039 | 3.5148
CCN, cache size 10000, first download | 1.2191 | 2.2816 | 4.0652
CCN, cache size 20000, first download | 1.3565 | 2.0619 | 3.3728
CCN, cache size 50000, first download | 1.0973 | 2.1711 | 3.4071
CCN, cache size 10, second download | 1.1317 | 2.5537 | 3.3352
CCN, cache size 5000, second download | 1.186 | 2.1755 | 3.401
CCN, cache size 10000, second download | 1.3815 | 2.178 | 3.4321
CCN, cache size 20000, second download | 1.305 | 1.3059 | 1.0896
CCN, cache size 50000, second download | 0.97762 | 1.582 | 1.3228

## Slide 14
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Achieved CCN bandwidths
Chart: Achieved CCN bandwidths
| CCN, cache size 10, first download | CCN, cache size 10, second download | CCN, cache size 5000, first download | CCN, cache size 5000, second download | CCN, cache size 10000, first download | CCN, cache size 10000, second download | CCN, cache size 20000, first download | CCN, cache size 20000, second download | CCN, cache size 50000, first download | CCN, cache size 50000, second download
0 ms delay | 0.20795 | 0.18375 | 0.17341 | 0.17534 | 0.17057 | 0.15053 | 0.1533 | 0.15935 | 0.1895 | 0.21271
100 ms delay | 0.095227 | 0.08143 | 0.090259 | 0.095587 | 0.091139 | 0.095474 | 0.10085 | 0.15923 | 0.095779 | 0.13145
200 ms delay | 0.061186 | 0.062349 | 0.059163 | 0.061143 | 0.051152 | 0.060588 | 0.061654 | 0.19084 | 0.061033 | 0.15721

## Slide 15
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
MTU (Maximum Transmission Unit) size and download time
Chart: Download time vs MTU
| 150 | 300 | 750 | 1500 | 3000
Download time [s] | 804.0039 | 784.2593 | 781.9538 | 806.6124 | 805.5986

## Slide 16
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Smart caching strategies

## Slide 17
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Smart caching strategies

## Slide 18
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Smart caching strategies

## Slide 19
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Packet delays in a scenario of smart caching
Links with losses
CCN network was unable to handle the file download
Strategy layer of CCNx does not implement handling of packet losses

## Slide 20: Conclusion and future work
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Our results showed some loopholes in the present implementation of CCNx like poor caching strategy, unable to handle packet losses and implementation flaws in MTU size.
For most of the real world scenarios, HTTP still has better performance compared to CCN, but CCN proved to outperform HTTP in the case of large cache sizes and multiple users/hosts requesting the same content data.
We also proposed smart caching strategies and other implementation changes required in the present CCNx.

## Slide 21
Titel van de presentatie 2
ET4169 - Microwaves, Radar and Remote Sensing Nov 2012 - Jan 2
2013
Our measurements were performed by simulating wide area network on a small scale network.
Such a simulation can not truly represent a wide area network like Internet where network traffic parameters change with time and space.
So, we would like to extend our measurements and test on more of a real world, wide area network (Internet) by using something like research test beds as in PlanetLab, as our future work.